## Slide 1: ATLAS small wheels and muon trigger upgrade
Osamu Sasaki
High Energy Accelerator Research Organization (KEK)
INPUTS from
RPC : S.Veneziano
sTGC : N.Lupu and G.Mikenberg
mMegas : V.Polychronakos
MDT : R.Richter and O.Sasaki

## Slide 2: Present system and improvement scenario

## Slide 3: RPC Barrel Upgrade in the Feet Region
LVL1 muon trigger efficiency in the feet sectors is about 50% lower than the one for standard sectors.
In order to recover the efficiency loss, a fourth layer of the RPC (RPC4) has been installed, wherever possible.
Improved to be 80% (pT = 20GeV).
RPC4

## Slide 4: Upgraded RPC system
Low pT & 1/2 coin.
h & f coin.
h : 3/4 coin.
f : 3/4 coin.
pT calculation
m
h : 3/4 coin.
f : 3/4 coin.
h & f coin.
RPC1
RPC2
RPC3
RPC4
Low-pT Pad
High-pT Pad
New Low-pT Pad
Sector Logic
MUCTPI
40 new Low-pT Pad boards with optical link and 56 splitter boards are needed.
It is under study how to handle the new trigger outputs in terms of sector logic and MUCTPI.

## Slide 5: Present detectors of SW + TGC of BW’s
2/3 coin.
hit position
3/4 coin.
track position and deviation
H-pT Board
R-f coin.
track fitting
pT calculation
Doublets TGC
Triplet TGC
Small Wheel
MDT + CSC
Doublet TGC
m
1/2 coin.
hit position
(VERY COARSE)
RoI, dR, df

## Slide 6: New detectors of SW + TGC of BW’s
track fitting
track position (R, f)
dq : deviation of incidence angle from infinite pT muons
2/3 coin.
hit position
3/4 coin.
track position and deviation
H-pT Board
R-f coin.
track fitting
crossing angle : b
pT calculation
Doublets TGC
Triplet TGC
Small Wheel
m
hit information (R, f) , dq
b
Precision Detector
s < 100mm
Level-1 Trigger angular resolution of incidence angle
< 1 mrad
Level-1 latency
RoI, dR, df

## Slide 7: Detector Candidates for the Small Wheel
aa

## Slide 8: TGC for LVL-1 and precision measurement
Each of the so-called TGC packages consists of 4 TGC gaps.
  Each gap contains 3 mm pitch strips (R), pad-wires (f) and pads for local trigger.
  ~400k independent electronics channels.
Time-over-Threshold signals from strips are used for precision measurement.
  The position resolution with better than 100mm has been demonstrated in test beam.
Hardware centroid circuits of the ToT signals are used for LVL-1 trigger.
Layer | σcorr(σnocorr )+/- ∆σ [μm]
1 new | 66.2 (120.9) +/- 1.2
2 new | 66.7 (79.8) +/-1.1
3 new | 63.55 (75.95) +/-0.96
4 new | 63.8 (116.4) +/-1.0
5 old | 144.6 (264.1) +/-2.5
6 old | 152.3 (182.1) +/-2.6
7 old | 163.6 (195.6) +/-2.6
8 old | 146.4 (267.2) +/-2.2

## Slide 10
TDC BLOCK DIAGRAM ( CONCEPT WHICH WORKS)
4 PH.
CLK.
GEN.
200 MHz
DIFF. CLK
400 MHz 4 PHASES CLK
0
90
180
270
COUNTER
COUNTER
COUNTER
COUNTER
SUMMING
12 BITS
CLK 0
CLK 90
CLK 180
CLK 270
ToTh
PULSE
12 BITS RESULT
of CONVERSION
THE ToTh INPUT PULSE WIDTH IS FROM
0 TO 255 ns

## Slide 11
COMPARATOR & SELECTOR to find the MAXIMUM CHARGE and its INDEX
Q0
Q1
Q2
Q14
Q2
Q15
/
8
Q max
ADDmax
Qmax-1
Q max+1
ADDmax -1
ADDmax +1
/
8
/
4
Compares the 16 Inputs
Finds the Maximum and
its Address.
Outputs the 3 groups of
numbers MAX and the 2
Adjacent groups.

## Slide 12
X
SIGMA
SIGMA
X
PROG. DELAY
X
X
ADDm-1
ADDm
ADDm+1
Qmax-1
Qmax
Qmax+1
/
CoM
STRIP PITCH 3500 um
BLOCK DIAGRAM of CENTER of MASS CALCULATION
DIVIDEND
DIVISOR
ADDi Relative address in the 16 strips slice
Qi Charge in units of TDC
/
4
/
12
/
16
/
16
/
12
/
28
/
12
/
12
/
28

## Slide 13: Additional latency calculation
The table shows the latency added by the insertion of the sTGC precision strip trigger logic into the existing path from the Inner Layer coincidence logic to the Sector Logic.
We take as a model the Xilinx Virtex6.
All numbers are estimates except that for the centroid finder for which a realistic design has been simulated.
Clock speed = ~400MHz
Yields 2.74/2.80msec latency (Existing = 2.55msec)
 | Min (ns) | Max (ns)
deskew | 25 | 25
ROI selector/ mpx | 10 | 15
serializer | 5 | 10
deserializer | 8 | 16
RLE | 16 | 24
latency for the last sample of the pulse | 64 | 64
find largest signal | 10 | 13
centroid of a layer | 25 | 35
centroid chooser | 10 | 12
centroid average | 5 | 8
tracklet calc (LUT) | 10 | 13
output serializer | 5 | 10
 | 193 | 245

## Slide 14: MicroMegas
2-layer + 2-layer (4 gaps in total) mMegas is foreseen.
  Charge information for precision measurement.
Two-dimensional readout per gap (2D MM)
  2 M channels in total.
Strips with 0.5mm pitch.
  The pitch is fine enough for LVL-1 trigger to reconstruct and find a track with the required resolution using simple discriminator outputs of hit signals. (Information of charge is not necessary.)
PCB
Mesh
Resistive strips
x strips
y strips

## Slide 15: Some desirable features for mMegas frontend
Real Time Peak Amplitude, Time Detection and on-chip ADC (10-12 bits?)
  Appropriate for a variety of detectors (mMegas, TGC, TPC, GEM, etc) requiring amplitude and time measurement
  on-detector zero suppression, dramatic reduction of data bandwidth
Neighbor channel enabling circuitry (allows relatively high thresholds without losing small amplitudes).
64/128 Channels/chip, simultaneous read/write with Derandomizing Buffers
Able to provide Trigger Primitives for possible on-detector track segment finding logic
  The address of the earliest cluster arrival associated with a given bunch crossing.
  Powerful zero-suppression scheme has to be designed to transmit Trigger Primitives to USA15.
  Address of the strips can be directly used in a Look-up-Table, similar to FTK, in USA15.
Detailed Specifications of back-end to be finalized.

## Slide 16: VMM1 IC Block Diagram (not yet finalized)
64 channels/chip, CMOS 130nm, 1.2V, MPW
adj. polarity, adj. gain (0.11 to 2 pC), adj. peaking time (25-200 ns)
derandomizing peak detection (10-bit) and time detection (1.5 ns)
real-time event peak trigger and address
integrated threshold with trimming, sub-threshold neighbor acquisition
integrated pulse generator, calibration circuits, analog monitor, channel mask and temperature sensor
continuous measurement and readout, derandomizing FIFO
few mW per channel, chip-to-chip (neighbor) communication, LVDS interface

## Slide 17: Small Tube MDT & TGC of SW + TGC of BW’s
hit signal alignment
2 x 3/4 coin.
2/3 coin.
hit position (R,f)
3/4 coin. Mx
track position (R,f) deviation (dR,df)
coin. Mx
track position (R,f) deviation (dR,df)
R-f coin. Mx
track fitting
crossing angle : b
pT calculation
Doublets TGC
Triplet TGC
Thin Tube MDT
& Doublet TGC
m
BCID signal
3/4 coin. Mx
track position (R,f) deviation (dR,df)
b
ASD + BCID (40MHz)
track position (R)
angle deviation (dq)

## Slide 18: BCID and Decoding circuits

## Slide 20: Station (4 x 2 layers) coincidence logic
3/4
0
1
2
3
4
n
n+1
n+2
n+3
………….
Aligned hit signals from each layer (1,2,3,4,5,6,7,8 layers) : 0.5mm step
Inner layers
The expected track deviations from infinite pT muons is less than ± 1o (pT > 20 GeV), so that one can restrict the track finding window within very narrow area. 3-out-of-4 and 3-out-of-4 coincidences are made for both super-layers individually. Information of position and deviation from both super-layers are combined.
The Level-0 trigger signal from TGC assists the track finding and the BCID.
The tracking efficiency, efficiency holes and the probability of the wrong tacking are to be estimated by the simulation works using real data.
Level-0
3/4
Super-layer 1
Super-layer 2
track position/deviation
track position/deviation
track position/deviation

## Slide 21: Latency Estimation (<3.2msec)
Present TGC Level-1 Trigger |  |  |  |  | Thin Tube MDT (SW) + TGC |  |  | 
 | nsec | CLK | Total CLK |  |  | nsec | CLK | Total CLK
TOF from interaction point to TGC | 65 | 2.5 | 2.5 |  | TOF from interaction point to SW (10 m) | 34 | 1.5 | 1.5
Propagation delay on wire/strip | 15 | 1 | 3.5 |  | Propagation delay along wire | 25 | 1 | 2.5
TGC response | 25 | 1 | 4.5 |  | MDT drift time (0 - 200 ns) |  | 8 | 10.5
ASD | 10 | 0.5 | 5 |  | ASD | 10 | 0.5 | 11
Cable to PS-Board (12.5m max.) |  | 2.5 | 7.5 |  | Bunch ID |  | 2 | 13
Variable Delay, Bunch ID, OR and signal routing |  | 2 | 9.5 |  | Serializer (TLK2501 @ 80MHz) + Optical Tx |  | 2 | 15
Variable Delay |  | 1 | 10.5 |  | Optical Fibre Cable (90m) |  | 18 | 33
3/4 Coincidence Matrix or 2/3 Coincidence Logic |  | 2 | 12.5 |  | Optical Rx + De-serializer (TLK2501 @ 80MHz) |  | 3 | 36
LVDS Tx (SN65LV1023) |  | 1 | 13.5 |  | Shift Register (28-steps, 0 - 200 ns) |  | 0 | 36
Cable to H-pT Board (15m max.) |  | 3 | 16.5 |  | coincidence |  | 2 | 38
LVDS Rx (SN65LV1224A) |  | 2 | 18.5 |  | track find |  | 2 | 40
Variable Delay |  | 1 | 19.5 |  | encoding |  | 1 | 41
H-pT Matrix |  | 2 | 21.5 |  | MDT (SW) – TGC(BW) combined HERE |  |  | 44
G-Link Tx (HDMP-1032A) + Optical Transmitter |  | 1.5 | 23 |  | TGC R-f coin. (LUT) MDT-TGC coin. |  | 3 | 47
Optical Cable to USA15 (90m max.) |  | 18 | 41 |  | crossing angle calculation |  | 3 | 50
Optical Receiver + G-Link Rx (HDMP-1034A) |  | 2.5 | 43.5 |  | pT calculation (LUT) |  | 3 | 53
Sector Logic |  | 7 | 50.5 |  | pT encoding |  | 1 | 54
Cable to MUCTPI (10m) |  | 2 | 52.5 |  | Cable to MUCTPI (10m) |  | 2 | 56
MUCTPI (4 + variable) |  | 11 | 63.5 |  | MUCTPI |  | 11 | 67
Cable to CTP (2.4m) |  | 0.5 | 64 |  | Cable to CTP (2.4m) |  | 0.5 | 67.5
CTP (5 + varable[0-11]) |  | 6 | 70 |  | CTP |  | 6 | 73.5
Cable to LTPi (10m) |  | 2 | 72 |  | Cable to LTPi (10m) |  | 2 | 75.5
LTPi + LTP + TTCvi + TTCex |  | 2 | 74 |  | LTPi + LTP + TTCvi + TTCex |  | 2 | 76.5
Variable Delay |  | 2 | 76 |  | Variable Delay |  | 2 | 78.5
Optical Cable to TGC frontend (110m) |  | 22 | 98 |  | Optical Cable |  | 22 | 100.5
TTCrq + fanout |  | 3 | 101 |  | TTCrq + fanout |  | 3 | 103.5
Cable to PS-Board (5m max.) |  | 1 | 102 |  | Cable to Frontend Electronics |  | 1.5 | 105
 |  |  | 2.55msec |  |  |  |  | 2.625msec

## Slide 22: Summary