Test of spatial resolution and trigger efficiency of a combined segment Thin Gap and Monitored Drift Tube Chambers for high luminosity LHC upgrades.

The results of a test of a device consisting of Thin Gap Chambers (TGC) and Monitored Drift Tubes (MDT) using the 180 GeV/c muons at the SPS-H8 muon beam at CERN are presented.
The aim of the test was to study the combined TGC-MDT system as tracking and triggering device in the ATLAS muon spectrometer after high-luminosity upgrades of the LHC. Two TGC quadruplets of 1.2 × 0.5 m2 size, containing four sensitive gaps, each providing pad, strip and wire readout, and a total thickness of 50 mm have been used. The TGC chambers show a position resolution of better than 70μm and an angular resolution of better than 0.4 mrad for 1.6 m distance between the two chambers.

The design of the drift tube chamber is based on the standard ATLAS muon precision (MDT) chambers, consisting of 6 or 8 layers of aluminum drift tubes with 30 mm outer diameter. The new developed chambers consist of 2 times 8 layers of 15 mm diameter aluminum tubes.
With the shorter maximum drift time of 200 ns, compared to about 700 ns now and the smaller tube cross section, the background occupancy is reduced by a factor of 7. At the same time the excellent spatial resolution of 40 μm per chamber is retained up to very high counting rates. A larger number of drift tube layers in the same detector volume offers improved redundancy and pattern recognition efficiency.

Signal from the TGC pads were used to provide trigger for the combined TGC-MDT device, where the MDT chamber was placed in between the two TGC quadruplets. The analysis of the recorded data shows a very good correlation between the TGC and MDT track position and inclination. The test allows to compare position and angular resolution of each system using the second as the reference. Also, the efficiency of the TGC pads as a triggering device has shown to be better than 99%.